## Slide 1: .
.
SRISHTI 2024
10TH NATIONAL LEVEL TECHNICAL PROJECT EXHIBITION & COMPETITION

## Slide 2: .
PROLONGED PRESERVATION OF HUMAN LIVER USING NORMOTHERMIC MACHINE PERFUSION PROCESS
TEAM MEMBERS
VISHWA B
YUVAPRABHA B
PRADEEP V
SUBHASH P
SANJEEVADHARSH B R

## Slide 3: Working Principle- Normothermic Perfusion
It is used in the field of Organ Transplantation to preserve and assess Human Organs
Normothermic Perfusion maintains Normal Temperature,Essential Substrates for Cellular Metabolism,Oxygen and Nutrition.
It provides continuous organ assessment for Real time Monitoring of Organ Function and Viability.

## Slide 4: Features of PNMP
PNMP Preserrves and assesses discarded human livers for Transplantation
Cold storage methods have limitations leading to the discard of viable organs
PNMP involves conditions oxygenated perfusion at normal Body Temperature

## Slide 5: Components Used:
.
Organ Basin:
Used to hold the Organs and protects the organs from Physical Trauma.
Organ Basin

## Slide 6: CLEANSER UNIT
.
Responsible for Cleaning and Filtering the organ Basin before and after it is used to preserve the organ.
Cleanser unit typically consists of filters and purification mechanisms that remove the unwanted particles,Bacteria and Other Contaminants from the Basin
.
CLEANSER UNIT

## Slide 7: AIR FILTERS
.
Air Filters remove the Carbondioxide and other waste gases from the perfusion System
It Maintains the Sterile Environment for the organ during the Perfusion Process.
AIR FILTER

## Slide 8: Heaters
.
Heaters are designed to keep the organs at a specific Temperature during Transportation from the donar to the Recipient
HEATER

## Slide 9: Reservoir
.
This Reservoir is designed to store and Protect the Liver during Transportation from the donal to the recipient.
The preservation Fluid such as University of Wisconsin(UW) Solution or Euro-Collins Solution is used.
RESERVOIR

## Slide 10: ROTAFLOW PUMP
.
Rotaflow Pump is a Medical Device designed for Extracorporeal Life Support Systems(ECLS) such as Extracorporeal Membrane Oxygenation(ECMO)
Operates in the Principle of Centrifugal Force to facilitate the movement of blood or other Fluid through pump.

## Slide 11: PV Pressure Monitor
.
Used to measure the Pressure Within the portal veins.
Changes in PV Pressure Indicate the Vascular Resistance and Congestion.

## Slide 12: Medication Probe
.
Used to dilate the Blood vessels and improve Blood Flow through the organ.
It maintains the Organ Functions and Reduce the risk of Ischemia

## Slide 13: PV Infection
.
The discarded human organ is connected to perfusion machine through its blood vessels,Including the portal vein.
The perfusion machine can deliver oxygen,Nutrients and other essential substances to the Organ.

## Slide 14: HA Infusion
.
It reduces the Inflammation and oxidative Stress during Organ Preservation,potentialy improve Organ function.
It is a hydsrophilic molecule which helps to maintain tissue hydration during PNMP.

## Slide 15: Work Flow

## Slide 16: Design Process: Step 1 - Creating Sketch

## Slide 17: Step- 2- Converting Sketch into Body
.
.

## Slide 18: Step -3 Assembling the Components